## Slide 1: BROCADE Overview UKNOF PRESENTATION
Julian Smith
January 20 2011

## Slide 2: Legal Disclaimer
All or some of the products detailed in this presentation may still be under development and certain specifications, including but not limited to, release dates, prices, and product features, may change. The products may not function as intended and a production version of the products may never be released. Even if a production version is released, it may be materially different from the pre-release version discussed in this presentation.
NOTHING IN THIS PRESENTATION SHALL BE DEEMED TO CREATE A WARRANTY OF ANY KIND, EITHER EXPRESS OR IMPLIED, STATUTORY OR OTHERWISE, INCLUDING BUT NOT LIMITED TO, ANY IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, OR NONINFRINGEMENT OF THIRD-PARTY RIGHTS WITH RESPECT TO ANY PRODUCTS AND SERVICES REFERENCED HEREIN.
Brocade, the B-wing symbol, BigIron, DCX, Fabric OS, FastIron, IronView, NetIron, SAN Health, ServerIron, and TurboIron are registered trademarks, and Brocade Assurance, DCFM, Extraordinary Networks, and Brocade NET Health are trademarks of Brocade Communications Systems, Inc., in the United States and/or in other countries. Other brands, products, or service names mentioned are or may be trademarks or service marks of their respective owners.

## Slide 3: LINX Update
Multiple issues seen on LINX core MLX platforms.
2 Devices running 5.0.0a code and 1 running 5.0.0c code.
5.0.0a is a privately available early adopter code release which covered bugs found by LINX in initial testing of 8x10G cards in April 2010.
LINX very early adopter of 8x10G blades for MLX. Tested first delivery blades in April and these were shipped to the UK from the test lab in San Jose.
Background

## Slide 4: LINX Update
Early November 1st instance of issue with low utilisation on individual port member of LAG occurs. Remedial action turn port off.
Upgrading the MLX’s from 4x10G to 8X10G cards a known bug was encountered. DEFECT000327663. Fixed in 5.0.0b.
Switchover between management cards causes packet loss on 8x10G modules. Known bug. DEFECT000308382. Fixed in 5.1.0 code
Issues Encountered

## Slide 5: LINX Update
Additional LAG ports showing the same low utilisation issue.
Packets on trunk from loan kit switch appearing mangled for some members peering sessions.
Hardware Failures on several 8x10G modules. Traffic managers showing unexpected drops. This has resulted in a number of RMA’s and movement of customer ports away from faulty blades. 1st RMA back with HQ for fault analysis.
Reset of 2 line cards due to TM errors
Issues Encountered

## Slide 6: LINX Update
Loan Kit put in place prior to December engineering moratorium.
Engineering have been involved in all issues associated with LINX from 2nd week of December with visibility at the highest levels of the organisation.
Short period of live network testing to try to track down underlying issue for low utilisation LAG ports. Unable to track down problem.
Escalation to CEO level within Brocade. Call’s between JS and all senior management team associated with issues.
Rectification Measures

## Slide 7: LINX Update
Three test rigs set up in QA labs to try to replicate outstanding LAG issue. Holidays cancelled over Christmas for a large number of Engineering staff to carry out testing. At this time none of the measures taken by Engineering have resulted in the issue being replicated.
Additional bugs also found by Engineering as part of the replication testing.
Daily update calls with customer by Critical Account Manager, Engineering and Account Team.
Rectification Measures

## Slide 8: LINX Update
Comprehensive plan put together for carrying out live analysis on misbehaving LAG port to try to get to the underlying issue. Scheduled Sunday night through Monday morning UK time.
It is anticipated that 5.0.0e will incorporate all the fixes for bugs found so far. If work on Sunday allows Brocade to replicate outstanding LAG issue a fix for this will also be included in 5.0.0e. If not discussions to be held with LINX on moving forward with code QA and release without this fix to cure all other issues encountered during the last 3 months.
Examining ‘Plan B’ options.
Moving Forward

## Slide 9: Thank You