## Slide 1: Juniper CALEA(LI)/Monitoring Solution Architectures
Richard Holben
rholben@juniper.net
UKNOF October, 2006

## Slide 2: Agenda
State of LI Worldwide
Juniper Core, Edge and Access solutions
Leveraging LI Needs
Summary
Questions

## Slide 3: State of LI Worldwide
United States
  1994 - Communications Assistance for Law Enforcement Act (CALEA) passed gives LEAs the authority for surveillance
  2001 - Patriot’s act expands power of LEAs to intercept IP-based communications
  2005 - FCC requirements extend govt reach on LI support
    The order requires that organizations like universities providing Internet access also comply with the law by spring 2007
    Additional potential legislation
Canada
  2005 - Canada’s "Modernization of Investigative Techniques Act" (MITA) Legislative Proposal
    Expect passage in 2006 with support required by spring 2007

## Slide 4: State of LI Worldwide (cont’d)
EMEA
  Nov 2005 - European Union committee agreed that details of all EU-wide phone calls & Internet use should be stored, but steps did not go as far as some members want in battle against terrorism/ crime.
  European Telecommunications Standards Institute (ETSI)
    Helping to drive standards that may also be adopted in Asia
APAC
  In Asia there's a wide range of legislation (or lack of) and practice
  1999 - The Japanese parliament passed legislation. Law has been in effect since August 1, 2000
  1979 - Telecommunications Intercept Act in Australia and updates
  2004 – Draft document on interception capabilities that will be provided by the carrier or carriage service provider (CCSP) to meet Govt Agencies requirements

## Slide 5: State of LI Worldwide (cont’d)
EMEA
  No legislation for LI yet except for Germany, UK and Netherlands
  EU directives on cyber crime provide legal basis for interception
  Every country expected to have its own law to comply with EU directives
  ETSI driving standards (see ETSI model below…)
Law Enforcement Agency
Access Network
Service Provider
Administration system
Intercept Related Mediation System
Content Mediation System
HI1: Warrant Related Information
HI2: Intercept Related Information
HI3: Content of communication
LEA Monitoring System

## Slide 6: Agenda
State of LI Worldwide
Juniper Core, Edge and Access solutions
Leveraging LI Needs
Summary
Questions

## Slide 7: Monitoring and Lawful Intercept Support
JFlow
Two Rx Interfaces used per fibre
Create flow records of a smaller percentage of traffic for offline analysis eg. a security service to identify anomalies or advanced accounting. M- and E-
Active Monitoring
using Production Routers
Passive Monitoring
using Overlay Passive routers
JFlow
Mediation
Control
Content Processing
Port Mirror
Lawful Intercept using Overlay Passive routers
Create summarized flow records of a high volume (100%) of traffic for offline analysis eg. a security service based on anomaly detection or advanced accounting.
Flow Analysis
Flow Analysis
Passive router filters IP addresses under surveillance. Forwards packets to Third Party content processing platform which extracts data authorized for agency.
Approach often preferred by core team. M-, T-
Active production router filters IP addresses under surveillance and port mirrors them to a Third Party content processing platform which extracts data authorized for agency. LI approach preferred at edge. M- and E-
LEA
Only Intercepted IP
App data
Lawful Intercept using Production routers
Mediation
Control
Content Processing
Filter forward
May be one router
May be one router
Only Intercepted IP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: JUNOS/M/T What is Active Monitoring?
Router (A) forwards packets and exports flow records
  Router (A) performs routing, forwarding, and exporting of flows
Monitors ingress or egress flows
Active Flow Monitoring
Flow export
Flow export
Passive Flow Monitoring
Router (A) forwards packets
Router (B) performs passive monitoring and exports flow records
  Router (B) does not participate in the control or data plane of network
Monitors multiple OC3, OC12, OC48s
B
A
A

## Slide 9: JUNOS/M/T What is Passive Monitoring?
Router (A) forwards packets and exports flow records
  Router (A) performs routing, forwarding, and exporting of flows
Monitors ingress or egress flows
Active Flow Monitoring
Flow export
Flow export
Passive Flow Monitoring
Router (A) forwards packets
Router (B) performs passive monitoring and exports flow records
  Router (B) does not participate in the control or data plane of network
Monitors multiple OC3, OC12, OC48s
B
A
A

## Slide 10: JUNOS/M/T Passive Monitoring: Packet Flow
Router (B) receives packets via port mirroring or probes
IP2 performs load distribution
  Each interface is associated with a monitoring group
  Traffic from the interfaces is load-shared among the PM-PICs in the monitoring group
  PM PICs export flow version 5 records
General Monitoring
Version 5 flow records
IP2
M-PIC
M-PIC
M-PIC
M-PIC
Router (B)
A
B

## Slide 11: JUNOSe / E Series Interface Mirroring
Supported as of JUNOSe 5.1
IP interfaces only (static or dynamic, but no LAC)
  Subscribers can be managed uniquely
Two new IP attributes introduced
  Mirror: All traffic will be mirrored to “Analyzer” port
  Analyzer: Does not support regular routed traffic and will drop all traffic entering the box via this interface
  Configured through CLI
  Security via privilege levels (16) in CLI
Analyzer port can be an IPSec or GRE tunnel, which ensures that mirrored data is transferred to Mediation Device without being routed

## Slide 12: JUNOSe and E series Interface Mirroring on E-Series
Recommendation
  Mirrored traffic should be less than 5% of total traffic for a given LC or chassis
Subscriber
IP Interface
Interface Attribute
Mirrored packets sent to Analyzer Port
Routing
Upstream
Interfaces

## Slide 13: Evolution of LI in JUNOSe
Support for dynamic IP and LAC interfaces
Introducing the concept of a “secure policy”, so LI becomes part of policy management
  Capability of attaching CLALCs (flow-based LI)
Attachment of secure policy through Radius Access Response and Radius Update Request (unsolicited)
  Support for COPS (SDX), SNMPv3 and CLI
Every Mirrored Packet will be pre-pended with
  UDP/IP header (will make mirrored packet routable)
  Interception ID and Acct-Session-ID (allows correlation of monitored user with mirrored data)

## Slide 14: JUNOSe/E Reference Model for Lawful Intercept (w/ Radius, DTAG)
l
a
t
i
g
i
d
BRAS
Mediation Device
H1: Control of LI
via Radius
H1: Control of LI
HI2: Data (control data)
HI3: Data (Intercepted Content)
HI3 data to LEA
HI2 data to LEA
Tunnel for HI3 data
Access Network
IP and LAC Interfaces
Mirror Points
Core
Radius Server/OSS
HI1 Warrant
Service Provider
LEA

## Slide 15: JUNOSe/E Concept of Secure Policies
“Secure Policies” allow only personnel with appropriate privilege to configure or display LI policy
Phase 1: Only one action (i.e. mirror) supported in “Secure Policy”
“Secure” Input and output policies for IP and L2TP
Attachment of Secure Policies through Radius in release Istanbul
  CLI and COPS support in future
Can be extended to be LI flow-based
Part of policy management – leverages smarts of Policy Manager

## Slide 16: Agenda
State of LI Worldwide
Juniper Core, Edge and Access solutions
Leveraging LI Needs
Summary
Questions

## Slide 17: Leveraging LI Needs
Cost-effective scaling of today’s LI solutions are required
Dedicated monitoring routers offload existing LI content processing from mediation platforms
Dedicated monitoring routers separate from production infrastructure simplifying operations
Provides base for revenue generating end-user services

## Slide 18: Implementations Today
Replicated
Data Over IPSEC or GRE Tunnel
Regional
Aggregation
Core
Peering
Router
E-Series
Replicating Router
LI Mediation suppliers eg: SS8, Top Layer etc.
Content Processing platforms usually proprietary hardware, admin and control on servers
Scale by adding Content Processing boxes
Frequently have limited interface support FE, limited SONET
LI Console
LI Content Processing
LI Content Processing
LI Content Processing
Replicated
Data

## Slide 19: Reducing Load on LI Content Processor
Replicated
Data Over IPSEC or GRE Tunnel
Regional
Aggregation
Core
Peering
Router
E-Series
Replicating Router
LI Console
LI Content Processing
Add M/T-Series Monitoring Router filter and reduce traffic processed by LI Content Processing Platform (less boxes)
The Monitoring Router Operates in “Passive Mode” and supports wider range of interfaces than LI Content Processing Platforms
M/T-Series
Monitoring Router
SONET ≤OC-48, ATM limited ALL DATA
FE/ GE Only data of Interest
Replicated
Data

## Slide 20: Separation of LI from Production Core Routers
Replicated
Data Over IPSEC or GRE Tunnel
Replicated
Data
Regional
Aggregation
Core
Peering
Router
E-Series
Replicating Router
LI Console
LI Content Processing
Monitoring Router is separate from core production routers
Keeps all filters and configuration related to LI separate from core production routers and removes visibility to operations staff
Proposed automation of filters on the Monitoring Router through SOAP/XML
Filter rule in XML
SOAP
SDX

## Slide 21: Leveraging LI Investments
Replicated
Data Over IPSEC or GRE Tunnel
Replicated
Data
Regional
Aggregation
Core
Peering
Router
E-Series
Replicating Router
LI Console
LI Content Processing
Monitoring Services PIC added to Monitoring Router
JFlow records created for all traffic or a sample eg only business monitoring service
Offline analysis of JFlow Records for Security anomaly detection, Traffic engineering and Capacity planning, Accounting
Filter rule x ≤100% of traffic
SOAP
SDX
Monitoring Services PIC
JFlow records
Offline analysis

## Slide 22: Summary
Junipers M/T/E, JUNOS and JUNOSe solutions provide the basis for flexible and powerful monitoring and LI solutions
Integrated solution portfolio provides both operational choice and capital efficiency
Effectively meet the needs of Lawful Intercept requirements
  Select, Replicate, Analyze and Distribute
Juniper Networks provides a solution that is available and is deployed today!

## Slide 23: Thanks!