## Slide 1: UK Spectrum
Steve Kennedy
NetTek Ltd

## Slide 2: Spectrum
Part of VHF Band III (174 - 230 MHz)
  This is part of the old VHF 425 line television bands. It is still used for television in parts of the world.
  Ofcom are proposing that sub-band 2 be used for PMR and sub-band 3 for T-DAB.

## Slide 3: Spectrum
Part of 410 – 425 MHz (410 - 415 MHz paired with 420 - 425 MHz) – see next
  2 x 5MHz bands which were part of the Dolphin Tetra1 network (now defunct).
Revised 412-414MHz paired with 422-424MHz
  The license will be issued on a technology neutral basis, though it is expected to be used for communications services such as PMR, PBR, emergency service and program making use.
  Any licensee must co-ordinate with RAF Flyingdales to ensure there is no interference to the military radar there that operates within this band. There is a 40Km exclusion zone around the base.
  Arqiva won all the licenses in this band, they paid just over £1.5m.

## Slide 4: Spectrum
470 – 862 MHz
  392MHz band which are the analogue TV bands. They exhibit good properties for radio transmission as equipment does not need to be line of site and penetrate buildings well.
  The government has mandated they are freed from analogue TV use by 2012, however there is no consensus as to what they should be used for in the future. Many countries still wish for them to be reserved for TV use well into the future (whether that is analogue or some digital variant).
  BBC wants the spectrum for HD terrestrial broadcasts.

## Slide 5: Spectrum
872 – 876 MHz paired with 917 - 921 MHz
  2 x 4MHz was allocated to Dolphin to be used for the Tetra2 network, but was released when Dolphin went into administration.
  Ofcom are proposing a single national technology neutral licence, however there are various licensed users below, between and above the band that will need to be protected.

## Slide 6: Spectrum
1452 – 1492 MHz
  40MHz (known as the L band) is used for DAB digital radio broadcasts in various parts of Europe. There are currently licensed users; however these licenses will be revoked by 2007 when Ofcom plan to make it available.
  Though parts of Europe are utilising the L band for DAB (as agreed by CEPT in Maastricht), Ofcom are not bound by this.
  They are proposing to license this in a technology neutral manner, however initial thoughts are 2 licenses of a single national license in the lower 12MHz, but with conditions to protect licensed satellite users in Europe and dividing the upper 28MHz into sub-bands which the licensees will determine use (expected DMB or DVB-H).

## Slide 7: Spectrum
GSM Guard Bands (1781.7 - 1785 MHz paired with 1876.7 - 1880 MHz)
  12 Licenses awarded
    Spring Mobile lowest bid £50,110
    COLT paid highest £1,513,218
Can be used to offer localised GSM (in-building) services.
15 channels.
Industry group to self-regulate.
  i.e. licensee interference issues.

## Slide 8: Spectrum

## Slide 9: Spectrum
1790 – 1798 MHz
  This band 8MHz is ideally suited for services such as mobile broadband and there have been approaches to Ofcom for new licenses.
  Unfortunately due to the complexity of this band (emergency services use, government trunk links for UK and Scottish Executive), Ofcom are not planning to release this 8MHz until issues can be worked out and existing license holders moved.

## Slide 10: Spectrum
2010 – 2025 MHz
  Part of the band, 10MHz in 2010 – 2020 MHz, is already designed for license exempt self-provided, self-coordinated IMT-2000 use (3G). However no use has been made for this purpose.
  It is possibly a good choice for WiMAX or mobile broadband services. Ofcom are therefore considering licensing the band in a 10MHz and 5MHz units, or maybe 3 x 5MHz units (5MHz may not be suitable for WiMAX, but 3 x 5MHz maybe) in a technology neutral approach. Since there is not a paired band it is only suitable for TDD systems, therefore Ofcom are considering pairing this band with 2290 – 2302 MHz (12MHz).
  Since 2010 – 2020 MHz is utilised in continental Europe for 3G use, there is likely to be interference on the south coast and north eastern coastal areas and Ofcom will have to safeguard the European users.

## Slide 11: Spectrum
2290 - 2302 MHz
  Potential to link this 12MHz band with above. It has been completely relinquished by the MoD and is newly available spectrum. If released as unpaired spectrum it can only be used for TDD technology.

## Slide 12: Spectrum
2302 – 2310 MHz
  This is the opposite leg to the 1790 – 1798 8MHz band and has the same issues.

## Slide 13: Spectrum
2500 – 2690 MHz
  Currently this is mainly used for video broadcast systems, all licensees have been given notice to vacate by 31st December 2006. This is a significant amount of spectrum (190MHz) which is greater than is currently allocated to the whole of 3G use (140MHz).
  Under European harmonisation it was expected to be allocated for 3G use, however Ofcom are considering a technology neutral license, but licensees would have to maintain 3G spectral masks to ensure there is no interference with UK and continental 3G networks.
  As a “3G” band, the MNO’s are likely to wish to have rights to it to take into account 3G network growth. If Ofcom are to consider this case, the band could not be made available until at after 2007/8 when the usage of 3G has advanced significantly to understand usage and growth requirements.

## Slide 14: Spectrum
  It was also potentially reserved for a new 3G entrant if competition in the UK didn’t work out with the existing one, however as “3” has established itself it is unlikely a new 3G entrant will be considered.
  This band is also well suited for WiMAX and mobile broadband use.
  Ofcom is proposing making the band available as a technology neutral license in 2008, if it gains approval at European level (as it is a harmonised band).
  BT already expressing interest.

## Slide 15: Spectrum
3.4GHz
  Ofcom auctioned 15 regional licenses for 3.4GHz and these were all acquired by UK Broadband (PCCW) – though Ofcom expected there would be other entrants PCCW stayed within the rules (at the time) and kept hold of the complete set.
  Currently the license only allows for fixed links; however the license is being changed to allow flexible usage (and mobility).
  This band is ideally suited to WiMAX and PCCW have started a service in the Reading and London areas.

## Slide 16: Spectrum
3.6 - 4.2 GHz (3695 - 3875 MHz paired with 4015 - 4195 MHz)
  There are already licensed users in this band including satellite up and down link systems.
  Pipex have a FWA 3605 - 3689 MHz paired with 3925 - 4009 MHz national license; however they have to coordinate with the existing licensed users so as not to interfere with them.
    Pipex acquired the license with the purchase of FirstNet (who acquired it from Tele2) and it was zero rated on Pipex’s books at the time of the acquisition.
    Pipex have recently received £21m from Intel Ventures to exploit the band for WiMAX use. The FWA license does not (currently) allow mobile use.
    Ripe for acquisition to provide an alternative local loop solution

## Slide 17: Spectrum
  The 3695 - 3875 MHz paired with 4015 - 4195 MHz (2 x 180MHz) would also be ideal for WiMAX.
  Ofcom is consulting on how best the spectrum should be utilised, including whether existing licensed users should remain.
  It is unlikely the band any decision will be made before 2006/2007 and auctioned after.

## Slide 18: Spectrum
5GHz
  The 5 GHz band is also an ISM band; however there are existing licensed users who have priority use of the band (mainly government and military satellite communications and military radar).

## Slide 19: Spectrum
10GHz (10.125 - 10.225 GHz paired with 10.475 - 10.575 MHz)
  10GHz was previously allocated to THUS (regionally) Cable and Wireless (nationally) and NTL (nationally), they have all relinquished their licenses, so Ofcom is planning to make the spectrum available as a single national technology neutral license of 2 x 100MHz bands.
  It will be suitable for use in point-to-point and point-to-multipoint applications, however there is limited equipment available, so it’s likely to be expensive which means it is likely to be used for network backhaul rather than connecting customers.
  The band does sit at the top end usable by WiMAX so if equipment does become available it could be used for FWA or WiMAX.
  Since there is licensed military use in this band, any licensee will be expected to coordinate use with the MoD so there is no interference to MoD users.
  Ofcom are consulting on this band and are proposing to auction it in 2007 for broadcasting use for video links and wireless cameras (2012 London Olympics), high-capacity, high-speed data connections for mobile and fixed broadband networks and broadband access networks.

## Slide 20: Spectrum
28 GHz (28.0525 - 29.4525 GHz)
  FWA licences in the 28 GHz band were auctioned in November 2000. 42 licences were on offer (three in each of 11 English regions, Scotland, Wales and Northern Ireland) and 15 were awarded following the auction:
  three in Greater London; three in Greater Manchester; three in the West Midlands; three in Northern Ireland; and four in Yorkshire, Northern England and Scotland.
  The reserve price for licenses varied from £100,000 to £4,000,000 (for London). One license in Northern Ireland has subsequently been returned.
  Ofcom will hold new auctions for the remaining licenses in-line with existing policy.
    Reserve price £50,000

## Slide 21: Spectrum
32 GHz Band (31.8 to 33.1 GHz)
  Though there is 1.3GHz (1300MHz) available Ofcom plan to offer either 1 national license of 2 x 500MHz or 2 national licenses of 2 x 250MHz in a technology neutral manner.
  The license(s) could be utilised for point-to-point or point-to-multipoint FWA networks. Due to the high frequencies the band is more likely to be used for backhaul services and only for line-of-sight. Equipment costs are likely to be high.
  Ofcom are consulting on this band and are proposing to auction it in 2007 for high-capacity, high-speed data connections for mobile and fixed broadband networks.

## Slide 22: Spectrum
40 GHz (40.5 to 43.5 GHz)
  Though there is 2GHz (2000MHz) available, Ofcom is considering an initial national license of 2 x 250MHz to “test the water” and see what innovative use will be made of it.
  Previous studies have shown that residential BFWA is not economical and though there was interest for MWS no one came forward with any proposals.
  Ofcom is planning to make proposals this year.

## Slide 23: Spectrum
71 – 76 GHz paired with 81 – 86 GHz
  Ofcom are proposing to make this paired band (2 x 5GHz i.e. 2 x 5000MHz) available under a light licensing regime (probably in a similar manner to the 5.8GHz Band C licensing).
  These frequencies will allow highly directional beams, and are only line of sight which means interference can be minimised.
  Ofcom’s consultation proposes links of up to 2Km under the regime.
  Due to the high frequencies, very high bandwidths can be supported (1 – 10GHz using current technology).

## Slide 24: Spectrum
  Unfortunately high frequency radio waves are highly ionising, which means there are likely to be health issues and they’ll only be used for point-to-point links (and possibly point-to-multipoint) away from humans i.e. on roof-tops.
  The equipment is also very expensive, so it’s unlikely to be a solution for broadband and will be used where businesses want to link buildings at LAN speeds.

## Slide 25: Thank you for listening!
Email: steve@nettek.co.uk